## Slide 1: Hardware Trojan: Observing the Invisible
Nathanael Weidler
Dallin Marshall
Sam Mitchell

## Slide 2: Objective
Leak the DES encryption key
Remove correlation between the key and the output
Remain undetected
Notes: How presentation will benefit audience: Adult learners are more interested in a subject if they know how or why it is important to them.
Presenter’s level of expertise in the subject: Briefly state your credentials in this area, or explain why participants should listen to you.

## Slide 3: Karri’s Taxonomy
Insertion stage
  Perpetrated by designer
Abstraction
  Gate level
Activation
  Input sequence
Effects
  Leak information
Location
  I/O Port
Notes: Lesson descriptions should be brief.

## Slide 4: The crime was committed
By the designer
At the gate level
With the candlestick

## Slide 5: Modified Taxonomy
Physical
  Size and threat model
Activation
  Triggering mechanism
Action
  Leakage method
Notes: Example objectives
At the end of this lesson, you will be able to:
Save files to the team Web server.
Move files to different locations on the team Web server.
Share files on the team Web server.

## Slide 6: Physical size
 | Baseline | Trigger | Trojan | Final
Flip Flops | 487 | 4 | 80 | 571
4-input LUT | 883 | 22 | 101 | 1006
Total logic elements | 1370 | 26 | 181 | 1577

## Slide 7: Trigger method
Sequence of plaintext least significant nibble (4 bits)
224 potential sequences
Testing will likely miss this by repeating or incrementing this nibble

## Slide 8: Key obfuscation
Targeted round key xor operation
  Input from Expansion Permutation
  Output
Leaked from round 9 of DES
Key correlation removed
  No additional logic required

## Slide 9: Leaking method: Back porch
Monitor displays plaintext and ciphertext
VGA display requires an offscreen buffer zone
  Called a front and back porch
Display by altering offscreen pixels

## Slide 10: Trojan output
Monitor displaying compromised data
Monitor sans shift

## Slide 11: Trojan output: 96 bits

## Slide 12: Key recovery
Xor 48-bit strings to obtain round key
Round key is a permuted version of original
Traverse permutations to 56-bit key
  8 bits are missing
Use 56-bit key guess to generate 64-bit key
Encrypt plaintext and compare ciphertexts

## Slide 13: Demo!

## Slide 14: Questions?

## Slide 15: Output bitstream